Low Power
#define LED_PIN 13
void setup() {
  pinMode(LED_PIN, OUTPUT);
  //Save Power by writing all Digital IO LOW - note that pins just need to be tied one way or another, do not damage devices!
  for (int i = 0; i < 20; i++) {
    if(i != 2)//just because the button is hooked up to digital pin 2
    pinMode(i, OUTPUT);
  }
  attachInterrupt(0, digitalInterrupt, FALLING); //interrupt for waking up
  //SETUP WATCHDOG TIMER
WDTCSR = (24);//change enable and WDE - also resets
WDTCSR = (33);//prescalers only - get rid of the WDE and WDCE bit
WDTCSR |= (1<<6);//enable interrupt mode
  //Disable ADC - don't forget to flip back after waking up if using ADC in your application ADCSRA |= (1 << 7);
  ADCSRA &= ~(1 << 7);
  //ENABLE SLEEP - this enables the sleep mode
  SMCR |= (1 << 2); //power down mode
  SMCR |= 1;//enable sleep
}
int i;

void loop() {
  digitalWrite(LED_PIN, HIGH);
  delay(1000);
  digitalWrite(LED_PIN, LOW);

for (i=0; i < 8; i++) { // 8 seconds WatchDog * 8 = 64 seconds
  //BOD DISABLE - this must be called right before the __asm__ sleep instruction
  MCUCR |= (3 << 5); //set both BODS and BODSE at the same time
  MCUCR = (MCUCR & ~(1 << 5)) | (1 << 6); //then set the BODS bit and clear the BODSE bit at the same time
  __asm__ __volatile__("sleep");//in line assembler to go to sleep
}

}
void digitalInterrupt(){
  //needed for the digital input interrupt
}
ISR(WDT_vect){
  //DON'T FORGET THIS! Needed for the watch dog timer. This is called after a watch dog timer timeout - this is the interrupt function called after waking up
}// watchdog interrupt

Video Low Power Arduino! Deep Sleep Tutorial - YouTube
tem 25 minutos e explica com reduzir usando os registradores do Arduino. Com um arduino . isolado, reduz para micro amperes e acorda com timer ou interrupcao
do Kevin Darrah. Tem varios outros videos.
https://www.patreon.com/kdarrah

Usando a biblioteca avr/sleep é possivel no Pro mini usar 200uA sleep e 5ma executando.

Aqui tem um exemplo com código
http://playground.arduino.cc/Learning/ArduinoSleepCode

Sorebe espe82266 tem o suiço
### #47 Power Saving with ESP8266 (Sleep Mode) Tutorial with some ...
Mostra os picos que é 74 mA e pode chegar a 0,2 mA sem fonte no modulo 12

tem os videos 091 e 64
para alimentar bem o esp82866 com baterias

#091 How to properly power the ESP8266 modules - YouTube

O canal dele é
https://www.youtube.com/channel/UCu7_D0o48KbfhpEohoP7YSQ